## Slide 1: OpenCV Basics Functions

## Slide 2: Basic Functions – Open Camera
cv2.VideoCapture(): create a video capture object
  cv2.VideoCapture(int index):
    Open a camera for a video capturing
    cv2.VideoCapture(-1): open raspy camera
    cv2.VideoCapture(0): open camera when you use desktop
    cv2.VideoCapture(1): open camera that is connected via USB (second camera)
  cv2.VideoCapture(const string &filename):
    Open a video file or image file sequences
    cv2.VideoCapture(‘Resources/Cars.mp4’)

## Slide 3: Basic Functions – Open Camera
Set resolution
  camera.set(3,640): Set width of the frames in the video stream as 640 px
  camera.set(4,480): Set height of the frames in the video stream as 480 px
  The parameter 3 and 4 is the enumeration taken from cv2.VideoCaptureProperties for set width and set height
  Check the full enumeration in the footer

## Slide 4: Basic Functions – Video from Camera
while(camera.isOpened()):
  Looping the program. The camera is already in open from cv2.VideoCapture()
camera.read():
  reading the current frame from camera
  this line is needed so the frames keep updating from the camera
cv2.flip(image,-1):
  Flipping the image, 3 possible parameters
    cv2.flip(image,0): vertical flipping
    cv2.flip(image,1): horizontal flipping
    cv2.flip(image,-1): flipping both axes

## Slide 5: Basic Functions – Video from Camera
cv2.imshow():
  to show the obtained image to a new window
  first parameter is the window name
  second parameter is the image object that is going to be shown
cv2.waitkey():
  display a window for given milliseconds or until any key is pressed
    cv2.waitkey(1): wait for 1 milliseconds or any key pressed
    cv2.waitkey(0): wait until key pressed
      useful when to show image for several seconds and automatically close the window
    if cv2.waitKey(1) == ord(‘q’)
      become true if the key ‘q’ is pressed, and exit the loop
cv2.destroyAllWindows():
  close any opened window after the exit the loop before the program is terminated

## Slide 6: Basic Functions – Change color space
Supposed we already have the image variable (image)
cv2.cvtColor(src,code):
  NOTES: there are more parameter besides src and code, we only use fundamental
  This function is to convert an image from a color space to another color space
  src: the image whose color space is to be changed (image in the left code)
  code: the color space code that we want for our image

## Slide 7: Basic Functions – Change color space

## Slide 8: Basic Functions – Change color space
Keep in mind that for colored images, OpenCV use BGR instead of RGB
colored images dimension
  (height,width,3)3 dimensions color
gray images dimension
  (height,width)1 dimension color
color space code:
  cv2.COLOR_BGR2GRAY: change BGR to gray
  cv2.COLOR_BGR2HSV: change BGR to HSV (hue saturation value) color space  easier for image processing
  cv2.COLOR_BGR2YUV: change BGR to YUV (Y: luma/brightness, U and V provide color information)  easier for machine learning

## Slide 9: Basic Functions – Image Filtering
To filter the color, it is a best practice to apply Gaussian blur to reduce the level of noise in the image
cv2.GaussianBlur():
  One method to apply filter
  first parameter: image that we want to apply filter
  second parameter: the size of kernel
  third parameter: Gaussian standard deviation value in X direction
cv2.threshold():
  If the value is smaller than the threshold, it is set to 0, otherwise it is set to a maximum value.
  The color value spans between 0 until 255 (0 means darkest color, 255 means brightest color)
  first parameter: image variable that we want to thresholding
  second parameter: threshold value
  third parameter: maximum value (set to 255 for the maximum value for color)
  fourth parameter: thresholding type
    The most useful one is cv2.THRESH_BINARY and cv2.THRESH_BINARY_INV

## Slide 10: Basic Functions – Image Filtering

## Slide 11: Basic Functions – Image Filtering
using cv2.THRESH_BINARY_INV
Original image is converted to gray space color image, and thresholding with 130 as the threshold value
 Results: object with value higher than 130 is filtered to black color (0 value)

## Slide 12: Basic Functions – Image Filtering
using cv2.THRESH_BINARY_INV
Original image is converted to gray space color image, and thresholding with 60 as the threshold value
 Results: only darker object is filtered

## Slide 13: Basic Functions – Image Filtering
using cv2.THRESH_BINARY
Original image is converted to gray space color image, and thresholding with 60 as the threshold value
 Results: only brighter object is filtered

## Slide 14: Contours

## Slide 15
img = cv2.imread('wkwk.png’)
open image “wkwk.png”
hsv = cv2.cvtColor(img, cv2.COLOR_BGR2HSV)
Convert image color space from BGR to HSV

## Slide 16
LowerRegion = np.array([hL,sL,vL],np.uint8)
upperRegion = np.array([hH,sH,vH],np.uint8)
Filter HSV picture according to desire range for yellow
146 < hue <= 243 176 < saturation <= 255
255 < value <= 255
HSV Colour_Filter
colour_filter = cv2.inRange(hsv,LowerRegion,upperRegion)
The color which inside range, will be 1 (white) and not inside the range will be 0 (black)
different colour, different range hue, saturation and value

## Slide 17
cv2.findContours()
Contours can be explained simply as a curve joining all the continuous points (along the boundary), having same color or intensity.
Real contour
cv2.drawContours(cnt, contours, -1, (0,255,0), 3)
Draw line according to continuous points in the contours

## Slide 18: Moment

## Slide 19
Until line number 24 the algorithm is same, that is color filter with desire range for a Red object
0 < hue <= 234 169 < saturation <= 255
188 < value <= 255

## Slide 20
cv2.morphologyEx()
closing small holes inside the
foreground objects
cv2.erode()
it erodes away the boundaries of
foreground object (Always try to
keep foreground in white)
cv2.dilate(red,kernal,iterations=1)
It is just opposite of erosion. Here,
a pixel element is '1' if at least
one pixel under the kernel is ‘1’

## Slide 21
kernal = np.ones((5,5),"uint8")
Setting kernel 5x5 pixel from color filter image
Noise Image
Clear Image
red = cv2.morphologyEx(redObject,cv2.MORPH_OPEN,kernal)
red = cv2.erode(red,kernal,iterations=1)
red = cv2.dilate(red,kernal,iterations=1)
Erase the noise below 5x5 pixel from color filter image, 5x5 is from kernel value

## Slide 22
M = cv2.moments(red)
Get the area (pixel group) from the object contour
if M["m00"] == 0:
cX = 0
cY = 0
else:
cX = int(M["m10"] / M["m00"]) get center position in X-coordinat
cY = int(M["m01"] / M["m00"]) get center position in Y-coordinat
cv2.circle() Draw Circle and text in central position
cv2.putText()
This algorithm is for find Center position of filtered object in XY-Coordinate